Nuclear Scattering Reactions in the Glauber Framework

Introduction:
Explain path to go:
→starting from elastic scattering at low energies
→going to medium to high energies
→ explain glauber: eikonal wave approximations, optical limit which leads to optical potential model, description via nucleon nucleon interaction

Elastic scattering at low energies:
Rutherford scattering→ poiniering works (alpha particle on gold atoms) – description in classical mechanics
Rutherford scattering only valid if coulomb potential
->at low energies below pion production only elastic cross section
→ introduce here the Scattering problem in quantum mechanics (see Schindler, p. 23)
→from classical physics we go to quantum mechanics and use partial wave decomposition
with theta being the scattering angle
→ include in this picture coulomb and nuclear interaction (as done in Kuk, papge 120)

Nuclear Density distribution studies via elastic scattering
→ Rutherford, Mott and Rosenbluth
→ show something about form Factors
→ how are charge radii and nuclear radii measured?

Glauber Model for nuclear scatering at high energies:

explain model assumption
→ eikonal wave approximation: -high incoming momentum
    - low scattering angle

Show picture of scattering

→ optical limit: - Nucleons at high energy → undeflected due to
large momentum (linear trajectory)
  -Nucleus large compared to nucleon-nucleon force
  -Motion of nucleons independent of nucleus
  -overall cross-section described in terms of nucleon-nucleon cross section

Description in the Probability Approach
(also here I use all the eiconal and optical limit approximation)

Description in the Eikonal optical-limit approximation

Comparison of both descriptions methods for tota interaction cross section→ should end up with same
Advantage of PA is that you can calculate the cross section for a defined number of removed projectile nucleons (Schindler, p. 49)

Extensions to the Glauber model
-things which cannot be neglected an influence the cross section
→ in medium modifications (see Lukas thesis)
→ Coulomb interaction
→ Pauli blocking

Cross sections for 12C + 12C:

→ Total reaction cross section
→ charge changing cross section → maybe I have to include lise++ calculations
→ isotope corrections- neutron removal → maybe I have to include lise++ calculations